Radio transmitters
Model train control:
RCS system
Author: Pierre Rouzeau copyright cc: by-nc-sa
Author is not linked with RCS system
- RCS handheld radio transmitters (throttles) are working in 27 MHz FM frequency with PCM coding.
- Transmitters of a train network shall use a unique radio frequency. In standard, this is 27.145 MHz. You can order equipment for others frequency, the only reasons changing being if one of your neighbour is using the same system or if there are parasites on standard frequency in your area.
- A transmitter is identified by an address defined with DIP switches among 64 possible addresses.
  This address is what links it to locomotives or accessories receivers.
- Transmitter is only active while pressing buttons. There is no watchdog to check the transmission.
- There can be multiple transmitters with the same address, in this case, they are linked to the same receivers.
- The address is the only parameter of a transmitter, there is no other setting nor configuration, which is done in receivers.
For each transmitter, there is three sets of commands, A, B and C.
The first command set (A) is sent while pressing directly one of the six first button (or a combination).
The two others command sets are sent while using the (B) or (C) buttons as ‘shift’ keys.
Each set of command is linked to a particular receiver, so one transmitter can be linked to three receivers.
There are 8 actions per command set, the action 7 being obtained by pressing both 1 & 3 ( & ) and action 8 by pressing 2 & 4 ( & ), with as needed shifting key for command set B or C.
Both kind of transmitter differs only by marking.
TX-24
S
TRC-TX-24
1 2 3 4
5 6 B C

---
Radio receivers
Radio receivers for electric locomotives drives motors up to 6 A/24V, direction lights and sound boards
They automatically links, while powered, with a transmitter sending a linking signal. To preserve links of other locomotives, their receivers shall be shut off.
Programming is done with the help of DIP switches and on/off sessions. 4 additional output could be added with a separated board.
Accessories radio receivers drive electronic signals or relays (1,2 or 4). They could be installed either in the train or on track side.
They are linked to the transmitter address and command set defined by DIP switches.
One command set (A, B or C) can drive an ensemble of receivers representing its 8 outputs.
Live steam receiver is no longer available.
Track power radio receiver adjust voltage on track (current 10A max).
There is no intelligent signal on the track, so there shall be only one locomotive per track. It shall be supplied with 14-24V DC current.
It is linked to transmitter in same manner as locomotive receiver.
Elite- X
Programming
Link to a transmitter emitting a linking signal.
Locomotive
receiver
TX address set
Accessories receiver
Accessory
latch
1-4
5-8
TRC-xx-X
Programming
Track receiver
TITAN-10x
Maxi

---
Two locomotives and two turnouts driven with only one throttle
A
B
C
Rx
Rx
27.145 MHz - PCM
Rx

---
Consist of two locomotives driven with
same signal, lamps on accessory receiver,
a third independant locomotive,
all driven with only one throttle
A
A
B
C
Rx
Rx
Rx
Rx

---
Separated Locomotives throttles with
two duplicated Accessories transmitters
3A
1B
1A
2A
2A
Separated transmitters are the
recommended solution because they are
less prone to false manipulation
and easy to exchange between train drivers.
You can label accessories transmitters
buttons.
1 transmitter costs 70 USD (60 Euros).
1
2
2
3
TRC-TX-24
1 2 3 4
5 6 B C
Rx
Rx
TRC-TX-24
1 2 3 4
5 6 B C
Rx
Rx

---
Only one locomotive supplied by track
track voltage being radio controlled
Filered Linear
14-24 V DC
A
No coding signal on track.
Only one locomotive or group per track.
Programming
Track receiver
TITAN-10x
Maxi

---
Electric locomotive example
with only one throttle
Track accessories
Electric loco
12-14V AC/DC
14.4 V (12 elements)
Accessories receiver
Group B
1-4
Accessory
latch
TX address set
Automatic link while powered when a TX send a linking signal.
Antenna
Elite- X
Programming
Fwd
Direct locomotive
command
Sound
board
Accessories command set
with (B)
Receiver
RX-8
Rev
Antenna
Motor 2
Motor 1
Acc
1
Acc
2
Acc
3
Acc
4
TX address (64 possible)
Acc